## Slide 1: Kelompok 19
Ferdyano (2406353723)
Mohamad Rizky Alamsyah (2406420892)
Valiant Joshua (2406352153)
Jesaya Hamonangan Gaudensius M.(2406409845)

## Slide 4
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity VGA is
generic (
H_TOTAL : integer := 800;
V_TOTAL : integer := 525
);
port (
clock_in : in std_logic;
reset_n : in std_logic;
h_output : out std_logic;
v_output : out std_logic;
x_out : out integer range 0 to H_TOTAL - 1;
y_out : out integer range 0 to V_TOTAL - 1;
video_on : out std_logic
);
end entity;

## Slide 5
architecture behavior of VGA is
constant H_VISIBLE : integer := 640;
constant H_FRONT : integer := 16;
constant H_SYNC : integer := 96;
constant H_BACK : integer := 48;
constant V_VISIBLE : integer := 480;
constant V_FRONT : integer := 10;
constant V_SYNC : integer := 2;
constant V_BACK : integer := 33;
-- H & V Count
signal h_count : integer range 0 to H_TOTAL - 1 := 0;
signal v_count : integer range 0 to V_TOTAL - 1 := 0;
begin

## Slide 6
process(clock_in, reset_n)
begin
if (reset_n = '0') then --reset asserted
h_count <= 0; --reset horizontal counter
v_count <= 0; --reset vertical counter
elsif rising_edge(clock_in) then
IF(h_count < H_TOTAL - 1) THEN --horizontal counter (pixels)
h_count <= h_count + 1;
ELSE
h_count <= 0;
IF(v_count < V_TOTAL - 1) THEN --veritcal counter (rows)
v_count <= v_count + 1;
ELSE
v_count <= 0;
END IF;
END IF;
end if;
end process;

## Slide 7
-- SYNC PULSE
h_output <= '0' when (h_count >= (H_VISIBLE + H_FRONT)) and
(h_count < (H_VISIBLE + H_FRONT + H_SYNC)) else '1';
v_output <= '0' when (v_count >= (V_VISIBLE + V_FRONT)) and
(v_count < (V_VISIBLE + V_FRONT + V_SYNC)) else '1';
-- Coordinates
x_out <= h_count;
y_out <= v_count;
-- VIDEO ON
video_on <= '1' when (h_count < H_VISIBLE) and (v_count < V_VISIBLE) else '0';
end behavior;

## Slide 8
https://youtu.be/_vS-kSauPwM

## Slide 9
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
use std.textio.all; -- Required for file writing
entity tb_bad_apple is
end tb_bad_apple;
architecture behavior of tb_bad_apple is
-- Component Declaration for the Unit Under Test (UUT)
component logic_unit
port(
clock : in std_logic;
reset : in std_logic;
vga_r : out std_logic_vector(3 downto 0);
vga_g : out std_logic_vector(3 downto 0);
vga_b : out std_logic_vector(3 downto 0);
vga_hs : out std_logic;
vga_vs : out std_logic
);
End component;
end component;
Testbench

## Slide 10
-- Inputs
signal clock : std_logic := '0';
signal reset : std_logic := '0';
-- Outputs
signal vga_r : std_logic_vector(3 downto 0);
signal vga_g : std_logic_vector(3 downto 0);
signal vga_b : std_logic_vector(3 downto 0);
signal vga_hs : std_logic;
signal vga_vs : std_logic;
-- Clock period definitions (50 MHz System Clock)
constant clock_period : time := 20 ns;
-- Pixel Clock (Derived from logic, but we know it is 25 MHz = 40 ns)
constant pixel_time : time := 40 ns;
-- Timing Constants (MUST MATCH YOUR VGA.VHD)
constant H_BACK : integer := 48;
constant V_BACK : integer := 33;
begin
-- Instantiate the Unit Under Test (UUT)
uut: logic_unit PORT MAP (
clock => clock,
reset => reset,
vga_r => vga_r,
vga_g => vga_g,
vga_b => vga_b,
vga_hs => vga_hs,
vga_vs => vga_vs
);

## Slide 11
-- Clock process definitions
clock_process :process
begin
clock <= '0';
wait for clock_period/2;
clock <= '1';
wait for clock_period/2;
end process;
-- Stimulus and Image Capture Process
stim_proc: process
file file_pointer : text;
variable line_el : line;
variable i, j : integer := 0;
variable r_int, g_int, b_int : integer;
begin
-- 1. Hold Reset for 100 ns
reset <= '0';
wait for 100 ns;
reset <= '1';
wait for 100 ns;
report "Rendering 200 Frames...";
for k in 1 to 200 loop
-- Wait for the frame to finish (Rising Edge of VSYNC)
wait until rising_edge(vga_vs);
report "Finished Frame: " & integer'image(k);
-- Now we are at the start of Frame 91.
-- The signals will now contain white data.
-- 2. Open the output file
file_open(file_pointer, "frame_" & integer'image(k) & ".ppm", write_mode);
-- 3. Write PPM Header
write(line_el, string'("P3"));
writeline(file_pointer, line_el);
write(line_el, string'("640 480"));
writeline(file_pointer, line_el);
write(line_el, string'("15"));
writeline(file_pointer, line_el);
-- 4. Sync to the START of the current frame
-- Since the loop above ended on a rising_edge (VSYNC End),
-- we are already perfectly positioned at the start of the Back Porch.
-- We can proceed directly to line skipping.

## Slide 12
-- 5. Skip the Vertical Back Porch lines
for i in 1 to V_BACK loop
wait until rising_edge(vga_hs);
end loop;
-- 6. Capture Visible Area (480 Lines)
for y in 0 to 479 loop
-- Wait for HSYNC to end (Start of Back Porch)
wait until rising_edge(vga_hs);
-- Wait through the Horizontal Back Porch
wait for H_BACK * pixel_time;
-- Capture one line of pixels (640 Pixels)
for x in 0 to 639 loop
-- Sample signals in the middle of the pixel
wait for pixel_time / 2;
r_int := to_integer(unsigned(vga_r));
g_int := to_integer(unsigned(vga_g));
b_int := to_integer(unsigned(vga_b));
write(line_el, integer'image(r_int) & " " & integer'image(g_int) & " " & integer'image(b_int) & " ");
wait for pixel_time / 2;
end loop;
writeline(file_pointer, line_el);
end loop;

## Slide 13
-- Close file and stop simulation
file_close(file_pointer);
report "Image Generation Complete! Frame " & integer'image(k) & " captured.";
end loop;
wait;
end process;
end behavior;

## Slide 14
Thank You